## Slide 1
Combinational Logic

## Slide 2: Combinational Logic
Logic circuits for digital systems may be combinational or sequential.
A combinational circuit consists of input variables, logic gates, and output variables.

## Slide 3: Design Procedure
The design procedure for combinational logic circuits are:
Determine required number of inputs and outputs from the specifications.
Derive the truth table for each of the outputs based on their relationships to the input.
Simplify the Boolean expression for each output. Use Karnaugh Maps or Boolean algebra.
Draw a logic diagram that represents the simplified Boolean expression.

## Slide 4: Half Adder
A combinational circuit that performs the addition of two bits is called a half adder.
The truth table for the half adder is listed below:
S = x’y + xy’
C = xy
x | y | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
0 | 1
1 | 0
0 | 0
0 | 1
S(x,y) = ∑m (1,2) C(x,y) = ∑m (3)
\
\
x
y
x
y

## Slide 5: Implementation of Half-Adder
S = x’y + xy’ or x⊕y
C=xy

## Slide 6: Full-Adder
One that performs the addition of three bits(two significant bits and a previous carry) is a full adder.
x | y | z | S | C
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
S(x,y,z) = ∑m (1,2,4,7) C(x,y,z) = ∑m (3,5,6,7)

## Slide 7: Simplified Expressions
S = x’y’z + x’yz’ + xy’z’ + xyz or (x⊕ y⊕z)
C = xy + xz + yz
C

## Slide 8: Full-Adder
S = x’y’z + x’yz’ + xy’z’ + xyz
= x’(y’z+yz’) + x(y’z’+yz)
= x’(y⊕z) + x(y⊕z)’ [y⊕z=A]
= x’A+xA’
= x⊕A
= (x⊕ y⊕z)

## Slide 9: Full-Adder
S = x’y’z + x’yz’ + xy’z’ + xyz
C = xy + xz + yz

## Slide 10: Full-Adder
x
y
z
S=(x⊕ y⊕z)
C = xy + xz + yz

## Slide 11: Half-Subtractor
One that performs the subtraction of two bits is half subtractor.
a | b | D | B
0 | 0 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
D(a,b) = ∑m (1,2) B(a,b) = ∑m (1)

## Slide 12: Half-Subtractor
D(a,b) = ∑m (1,2) B(a,b) = ∑m (1)

## Slide 13: Half-Subtractor
A⊕B
A’B
B
A’

## Slide 14
One that performs the subtraction of three bits is Full subtractor.
D(a,b,c) = ∑m (1,2,4,7) B(a,b,c) = ∑m (1,2,3,7)
a | b | c | D | B
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
Full-Subtractor

## Slide 15
D(a,b,c) = ∑m (1,2,4,7) B(a,b,c) = ∑m (1,2,3,7)
a
bc
a
bc
Difference(D)=a⊕b⊕c
Borrow(B)=a’c+bc+a’b
Full-Subtractor

## Slide 16
Full-Subtractor
a
b
c
D=a⊕b⊕c
B=a’c+bc+a’b

## Slide 17
a b c
D=a⊕b⊕c
B=a’c+bc+a’b
b
a’
c
a’
b
c
Full-Subtractor

## Slide 18
Design a full adder circuit using two half adders. Also verify your answer.
Full Adder
S=(x⊕ y⊕z)
C = xy + xz + yz
Half Adder
S=(x⊕ y)
C = xy
From above circuit:
S = (x⊕ y⊕z)
C = xy+z (x⊕ y)
= xy+z(x’y+xy’)
= xy+x’yz+xy’z
From actual Full adder circuit:
C = xy + xz + yz
C = xy + xz(y+y’) + yz(x+x’)
C = xy+xyz+xy’z+xyz+x’yz
C = xy+xyz+xy’z+x’yz
C = xy(1+z)+xy’z+x’yz
C = xy+x’yz+xy’z

## Slide 19
Construct a full subtractor circuit using two half
subtractors. Also verify your answer.
From above circuit:
B = x’y+z (x⊕y)’
B = x’y+z(xy+x’y’)
B = x’y+xyz+x’y’z
But from the actual Full subtractor circuit:
B = x’y+yz+x’z
B = x’y+yz(x+x’)+x’z(y+y’)
B = x’y+xyz+x’yz+x’yz+x’y’z
B = x’y+xyz+x’yz+x’y’z
B = x’y+x’yz+xyz+x’y’z
B = x’y(1+z)+xyz+x’y’z
B = x’y. +xyz+x’y’z verified.
x
y
z
D= (x⊕ y⊕z)
B= x’y+z (x⊕y)’

## Slide 20
Design a converter circuit which converts BCD to excess 3.
Don’t care conditions:
m10-m15
W(A,B,C,D) = ∑m (5,6,7,8,9)
X(A,B,C,D) = ∑m (1,2,3,4,9)
Y(A,B,C,D) = ∑m (0,3,4,7,8)
Z(A,B,C,D) = ∑m (0,2,4,6,8)
Code Conversion Circuit

## Slide 21
W(A,B,C,D) = ∑m (5,6,7,8,9) X(A,B,C,D) = ∑m (1,2,3,4,9)
W=A+BC+BD X=B’C+B’D+BC’D’
Code Conversion Circuit

## Slide 22
Y(A,B,C,D) = ∑m (0,3,4,7,8) Z(A,B,C,D) = ∑m (0,2,4,6,8)
Y=CD+C’D’ Z=D’
Code Conversion Circuit

## Slide 23
BCD to Excess-3 Code Converter Logic Diagram
Code Conversion Circuit

## Slide 24
Design a converter circuit
which converts Binary to Gray.
W(A,B,C,D) = ∑m (8,9,10,11,12,13,14,15)
X(A,B,C,D) = ∑m (4,5,6,7,8,9,10,11)
Y(A,B,C,D) = ∑m (2,3,4,5,10,11,12,13)
Z(A,B,C,D) = ∑m (1,2,5,6,9,10,13,14)
Code Conversion Circuit

## Slide 25
Code Conversion Circuit

## Slide 26
Parity Generator Circuit
EVEN PARITY
P(A,B,C) = ∑m (1,2,4,7)

## Slide 27
Parity Generator Circuit
P(A,B,C) = ∑m (1,2,4,7)
3 bit even parity generator circuit
P
A
B
C

## Slide 28
Parity Generator Circuit
ODD PARITY
P(A,B,C) = ∑m (0,3,5,6)

## Slide 29
Parity Generator Circuit
P(A,B,C) = ∑m (0,3,5,6)
P=A’B’C’+A’BC+AB’C+ABC’
P=C’(A’B’+AB)+C(A’B+AB’)
P=C’ (A⊕B)’ + C (A⊕B)
P=C’X’ + CX [X= (A⊕B)]
P=C⊙X
P=C⊙(A⊕B)
P= (A⊕B) ⊙ C
3 bit odd parity generator circuit
A
B
C
P

## Slide 30
Parity Checker Circuit
Even Parity
Check
Cp(A,B,C,P) =
∑m (1,2,4,7,8,11,13,14)
Cp=1 for error

## Slide 31
Parity Checker Circuit
Cp(A,B,C,P) = ∑m (1,2,4,7,8,11,13,14)
Cp= (A⊕B)⊕(C⊕P)

## Slide 32
Parity Checker Circuit
A
B
C
P
Cp
3 bit message even parity checker circuit

## Slide 33
Parity Checker Circuit
Odd Parity
Check
A
B
C
P
Cp
3 bit message odd parity checker circuit
Cp= (A⊕B) ⊙(C⊕P)

## Slide 34
Design a converter
circuit which converts
84 -2 -1 to 2421 code.
Code Conversion Circuit
Decimal | 8 4 -2 -1 | 2 4 2 1
 | A B C D | W X Y Z
0 | 0 0 0 0 (m0) | 0 0 0 0
1 | 0 1 1 1 (m7) | 0 0 0 1
2 | 0 1 1 0 (m6) | 0 0 1 0
3 | 0 1 0 1 (m5) | 0 0 1 1
4 | 0 1 0 0 (m4) | 0 1 0 0
5 | 1 0 1 1 (m11) | 1 0 1 1
6 | 1 0 1 0 (m10) | 1 1 0 0
7 | 1 0 0 1 (m9) | 1 1 0 1
8 | 1 0 0 0 (m8) | 1 1 1 0
9 | 1 1 1 1 (m15) | 1 1 1 1
Don’t care conditions:
m1,m2,m3,m12,m13,m14
W(A,B,C,D) = ∑m (8,9,10,11,15)
X(A,B,C,D) = ∑m (4,8,9,10,15)
Y(A,B,C,D) = ∑m (5,6,8,11,15)
Z(A,B,C,D) = ∑m (5,7,9,11,15)

## Slide 35
Design a converter
circuit which converts
84 -2 -1 to 2421 code.
Code Conversion Circuit

## Slide 36
Design a converter
circuit which converts
84 -2 -1 to 2421 code.
Code Conversion Circuit

## Slide 37
Design a converter
circuit which converts
84 -2 -1 to 2421 code.
Code Conversion Circuit

## Slide 38
Design a converter
circuit which converts
84 -2 -1 to 2421 code.
Code Conversion Circuit

## Slide 39: Seven Segment Display

## Slide 40: Seven Segment Display
7 LEDs (light emitting diodes), each one controlled by an input.
A seven-segment decoders can be used to display the decimal numbers 0-9 and some alpha characters.

## Slide 41: Display Possibilities
Simple Messages
Select Alpha Characters

## Slide 42: Seven Segment Display
Input is a 4-bit BCD code  4 inputs (A, B, C, D)
Output is a 7-bit code (a,b,c,d,e,f,g) that allows for the decimal equivalent to be
Displayed Example:
– Input: (0000)BCD
– Output: 1111110 (a=b=c=d=e=f=1, g=0)
d
a
b
c
e
f
g

## Slide 43: Applications

## Slide 44: Truth Table for 7 Segment Decoder

## Slide 45: Expression for segment g
g (A,B,C,D) = ∑m (2, 3, 4, 5, 6, 8, 9) and ∑d (10,11,12,13,14,15)

## Slide 46: Draw K MAP for all the 7 expressions: a,b,c,d,e,f,g and draw the logic diagram