## Slide 1
Sequential Logic

## Slide 2: Sequential Circuits
The outputs of the circuit will depends upon the present inputs as well as on the sequence of the previous outputs of the circuits.
It is basically combination of combinational circuit and memory unit.

## Slide 3: Sequential Circuits
Combinational Circuit | Sequential Circuit
Logic gates are the basic elements used. | Flip flops are the basic elements used.
It consists of input, output variables and logic gates inter connection. | It consists of input, output variables ,logic gates inter connection and memory unit.
No memory unit present. | Present
Outputs can be calculated from the function with input. | Output depends upon present inputs as well as past outputs.
Input triggers the combinational circuit. | Clock pulse and previous outputs triggers the S C

## Slide 4: Latch
Latch is storage device. A latch is constructed from the cross coupled NAND or NOR gates.
The outputs of Latch are compliment of each other.
i.e. Q≠Q’

## Slide 5: SR Latch
SR latch using NOR gates
A | B | F
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Case I
When S = 1 and R =0; Q = 1 and Q’ = 0
When S = 0 and R = 0; Q = 1 and Q’ = 0 ( Memory)
Case II
When S = 0 and R = 1; Q = 0 and Q’ = 1
When S = 0 and R = 0; Q = 0 and Q’ = 1 (Memory)
Case III
When S = 1 and R = 1; Q = 0 and Q’ = 0 [Not Used]
S | R | Q | Q’
0 | 0 | 1 | 1
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | Not used | Not used

## Slide 6: SR Latch
SR latch using NAND gates
S
R
Q
Q’
A | B | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
S | R | Q | Q’
0 | 0 | Not used | Not used
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | Memory | Memory

## Slide 7: Clock Pulse and Triggering
Varying Signal that triggers or control the operation of Flip flops.
Triggering Methods
Level Triggering
Edge Triggering

## Slide 8: SR Flip Flop
Clk
S* | R* | Q | Q’
0 | 0 | Not used | Not used
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | Memory | Memory
TT of SR latch using NAND

## Slide 9
Clk | S | R | Q | Q’
0 | x | x | Mem | Mem
1 | 0 | 0 | Mem | Mem
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | Invalid | Invalid
TT of SR flip flop

## Slide 10: SR Flip Flop
Clk | S | R | Q n+1
0 | x | x | Qn
1 | 0 | 0 | Qn
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | Not used
Truth table of SR flip flop
Characteristics table of SR flip flop
Qn | S | R | Q n+1
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | x
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | x
Qn | Q n+1 | S | R
0 | 0 | 0 | x
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | x | 0
Excitation table of SR flip flop
Qn+1 = QnR’ + S

## Slide 11: D Flip Flop
S
R
Clk | S | R | Q n+1
0 | x | x | Qn
1 | 0 | 0 | Qn
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | Not used
Clk | D | Qn+1
0 | x | Qn
1 | 0 | 0
1 | 1 | 1
TT of SR flip flop
TT of D flip flop

## Slide 12: D Flip Flop
Clk | D | Qn+1
0 | x | Qn
1 | 0 | 0
1 | 1 | 1
TT of D flip flop
Qn | D | Qn+1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
Characteristics of D flip flop
Qn+1 = D
Qn | Qn+1 | D
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
Excitation of D flip flop

## Slide 13: JK Flip Flop
CLK | S | R | Qn+1
0 | X | X | Qn
1 | 0 | 0 | Qn
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | Invalid
T.T for S-R Flip-Flop
CLK | J | K | Qn+1
0 | X | X | Qn
1 | 0 | 0 | Qn
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | Q’n
T.T for J-K Flip-Flop
Toggling

## Slide 14: JK Flip Flop

## Slide 15: T Flip Flop
CLK | J | K | Qn+1
0 | X | X | Qn
1 | 0 | 0 | Qn
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | Qn’
T.T for J-K Flip-Flop
CLK | T | Qn+1
0 | X | Qn
1 | 0 | Qn
1 | 1 | Q’n
T.T for T Flip-Flop

## Slide 16: T Flip Flop
CLK | T | Qn+1
0 | X | Qn
1 | 0 | Qn
1 | 1 | Qn’
T.T for T Flip-Flop
Qn | T | Qn+1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Characteristics table for T Flip-Flop
Qn | Qn+1 | T
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Excitation Table for T Flip-Flop

## Slide 17: JK Flip Flop
CLK | J | K | Qn+1
0 | X | X | Qn
1 | 0 | 0 | Qn
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | Q’n
T.T for J-K Flip-Flop
Qn | J | K | Qn+1
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Characteristics Table for J-K Flip-Flop
Qn | Qn+1 | J | K
0 | 0 | 0 | x
0 | 1 | 1 | x
1 | 0 | x | 1
1 | 1 | x | 0
Excitation table for J-K Flip-Flop

## Slide 18: Master - Slave JK Flip Flop
Combination of 2 JK flip-flops in series.
One acts as ‘master’ and the other as ‘slave’
It also includes an Inverter(Not Gate).

## Slide 19: Master Slave JK Flip Flop

## Slide 20: Master Slave JK Flip Flop
When the clock is high, master is operational but slave is not operational(it will keep memory)
When the clock is low, master is not functional but slave is. The output at slave is fed back to master but the clock is low. So, In this case effect of feedback is eliminated(which eliminates racing)
CLK | J | K | Qn+1
0 | X | X | Qn
1 | 0 | 0 | Qn
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | Q’n
T.T for J-K Flip-Flop

## Slide 21: Conversion of Flip-Flop (Realization of one Flip-Flop using other Flip-Flop)
Steps for Flip-Flop Conversion
Make Characteristics table for required flip-flop.
Make Excitation table for available flip-flop.
Write Boolean expression for available flip-flop.
Draw the Block Diagram.

## Slide 22: Example 1 – JK to D
Required flip-flop : D, Available flip-flop : JK
Qn | D | Qn+1 | J | K
0 | 0 | 0 | 0 | x
0 | 1 | 1 | 1 | x
1 | 0 | 0 | x | 1
1 | 1 | 1 | x | 0
Qn | Qn+1 | J | K
0 | 0 | 0 | x
0 | 1 | 1 | x
1 | 0 | x | 1
1 | 1 | x | 0
Char table of D ( required f/f))
Using K map
J = D
K = D’
Excitation table of JK ( available f/f))
J
K
Qn
Q’n
D
D’
Clk

## Slide 23: Example 2 – SR to JK
Required flip-flop : JK, Available flip-flop : SR
Qn | J | K | Qn+1 | S | R
0 | 0 | 0 | 0 | o | x
0 | 0 | 1 | 0 | 0 | x
0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 1 | x | 0
1 | 0 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | x | 0
1 | 1 | 1 | 0 | 0 | 1
Qn | Qn+1 | S | R
0 | 0 | 0 | x
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | x | 0
From K map
S = Qn’J R = QnK

## Slide 24: Example 3 – T to D
Required flip-flop : T Available flip-flop : D

## Slide 25: Direct Inputs
Also called asynchronous inputs.
Flip-flop have control over the outputs (Q and Q’) regardless of clock signal.
These inputs are called the preset (PRE) and clear (CLR).
When preset = 0, Q equals to 1
When clear = 0, Q equals to 0

## Slide 26: State Diagram and State Table
P.S
N.S
x/y
x=input
y=output
Qn
Qn+1
The relationship that exists among the inputs, outputs, present states and next states can be specified by either the State Diagram or State Table.

## Slide 27
Obtain the state table.
Reduce the no. of state using state reduction method(If possible)
Do state assignment(If required)
Determine the number of flip flop required.
Derive circuit excitation table from state table/diagram.
Obtain the expression for circuit output and flip flop output.
Implement the circuit.
Design Procedure for Sequential Circuit

## Slide 28: State Reduction and Assignment

## Slide 29
Present State | Next State |  | Output | 
 | x=0 | x=1 | x=0 | X=1
A | B | C | 1 | 0
B | F | D | 0 | 0
C | D | E | 1 | 1
D | F | E | 0 | 1
E | A | D | 0 | 0
F | B | C | 1 | 0
Present State | Next State |  | Output | 
 | x=0 | x=1 | x=0 | X=1
A | B | C | 1 | 0
B | A | D | 0 | 0
C | D | E | 1 | 1
D | A | E | 0 | 1
E | A | D | 0 | 0

## Slide 30
Present State | Next State |  | Output | 
 | x=0 | x=1 | x=0 | X=1
A | B | C | 1 | 0
B | A | D | 0 | 0
C | D | B | 1 | 1
D | A | B | 0 | 1
A
C
B
D
0/1
1/0
0/1
1/0
0/0
1/1
1/1
0/0
0/1
1/0
0/1
1/0
0/0
1/1
1/1
0/0
00
10
11
01

## Slide 31
1/1
1/0
0/0
0/0
1/0
00
01
11
10
1/0
0/1
0/0
Present State |  | Next State |  |  |  | Output | 
 |  | x=0 |  | x=1 |  | x=0 | X=1
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 0 | 0
Design a sequential circuit from the following state diagram using T flip-flop.

## Slide 32
Present State |  |  | Next State |  | Output (y) | Using T f/f | 
Qa | Qb | x | Qa+ | Qb+ |  | Ta | Tb
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
1/1
1/0
0/0
0/0
1/0
00
01
11
10
1/0
0/1
0/0
Ta = Qa’.Qb.x’ +Qa.Qb’x
Tb = Qa’.Qb’.x + Qa.Qb.x’
Y = Qa.Qb’.x’ + Qa. Qb’ . x
= Qa.Qb’(x+x’)
= Qa.Qb’

## Slide 33
Ta = Qa’.Qb.x’ +Qa.Qb’x
Tb = Qa’.Qb’.x + Qa.Qb.x’
Y = Qa.Qb’.x’ + Qa. Qb’ . x
= Qa.Qb’(x+x’)
= Qa.Qb’

## Slide 34
1/1
1/0
0/0
0/0
1/0
00
01
11
10
1/0
0/0
0/0
From the state diagram given below, Design a Sequential circuit using
SR flip-flop.
Present State |  |  | Next State |  | Output (y) | Using SR f/f |  |  | 
Qa | Qb | x | Qa+ | Qb+ |  | Sa | Ra | Sb | Rb
0 | 0 | 0 | 0 | 0 | 0 | o | x | 0 | x
0 | 0 | 1 | 0 | 1 | 0 | 0 | x | 1 | 0
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | x | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | x | x | 0
1 | 0 | 0 | 1 | 0 | 0 | x | 0 | 0 | x
1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | x | x
1 | 1 | 0 | 1 | 0 | 0 | x | o | 0 | 1
1 | 1 | 1 | 1 | 1 | 0 | x | 0 | x | 0

## Slide 35
Present State |  |  | Next State |  | Output (y) | Using SR f/f |  |  | 
Qa | Qb | x | Qa+ | Qb+ |  | Sa | Ra | Sb | Rb
0 | 0 | 0 | 0 | 0 | 0 | o | x | 0 | x
0 | 0 | 1 | 0 | 1 | 0 | 0 | x | 1 | 0
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | x | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | x | x | 0
1 | 0 | 0 | 1 | 0 | 0 | x | 0 | 0 | x
1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | o | x
1 | 1 | 0 | 1 | 0 | 0 | x | o | 0 | 1
1 | 1 | 1 | 1 | 1 | 0 | x | 0 | x | 0
Sa(Qa,Qb,x) = Σ (2) & d(Qa,Qb,x) = Σ (4,6,7)
Ra(Qa,Qb,x) = Σ (5) & d(Qa,Qb,x) = Σ (0,1,3)
Sb(Qa,Qb,x) = Σ (1) & d(Qa,Qb,x) = Σ (2,3,7)
Rb(Qa,Qb,x) = Σ (6) & d(Qa,Qb,x) = Σ (0,4,5)
y(Qa,Qb,x) = Σ (5)

## Slide 36
Sa(Qa,Qb,x) = Σ (2) & d(Qa,Qb,x) = Σ (4,6,7)
Sa = Qbx'
Sb(Qa,Qb,x) = Σ (1) & d(Qa,Qb,x) = Σ (2,3,7)
Sb = Q'ax
Rb(Qa,Qb,x) = Σ (6) & d(Qa,Qb,x) = Σ (0,4,5)
Rb = Qax'
Ra(Qa,Qb,x) = Σ (5) & d(Qa,Qb,x) = Σ (0,1,3)
Ra = Q'bx

## Slide 37
y(Qa,Qb,x) = Σ (5)
y = QaQ'bx
y = QaQ'bx
Sa = Qbx'
Sb = Q'ax
Ra = Q'bx
Rb = Qax'

## Slide 38
y = QaQ'bx Sa = Qbx' Sb = Q'ax Ra = Q'bx Rb = Qax'

## Slide 39
1/0
1/0
0/1
1/0
1/1
00
01
11
10
0/1
0/0
0/1
Design a sequential circuit from the following state diagram using S-R flip-flop.