## Slide 1
Number Systems

## Slide 2
Decimal Number System
 Base (also called radix) = 10
 10 digits { 0, 1, 2, 3, 4, 5, 6, 7, 8, 9
 Digit Position
 Integer & fraction
 Digit Weight
}
2
1
0
-1
-2
Position
 Weight = (Base)
 Magnitude
100
10
1
0.1
0.01
 Sum of “Digit x Weight”
 Formal Notation
500
10
2
0.7
0.04
2
1
0
-1
-2
d2*B +d1*B +d0*B +d-1*B +d-2*B
(512.74)10
4
7
2
1
5

## Slide 3
Octal Number System
 Base = 8
 8 digits { 0, 1, 2, 3, 4, 5, 6, 7
 Weights
}
Position
64
8
1
1/8 1/64
 Weight = (Base)
 Magnitude
 Sum of “Digit x Weight”
 Formal Notation
2
5 *82+1
1
0
-1
-2
*81+2 *80+7
*8-1+4 *8-
2
=(330.9375)10
(512.74)8
4
7
2
1
5

## Slide 4
Binary Number System
 Base = 2
 2 digits { 0, 1 }, called binary digits or “bits”
 Weights
4
2
1
1/2
1/4
Position
 Weight = (Base)
 Magnitude
 Sum of “Bit x Weight”
 Formal Notation
2
1 *22+0
1
0
-1
-2
*21+1 *20+0
*2-1+1 *2-
2
 Groups of bits
4 bits = Nibble
8 bits = Byte
=(5.25)10
(101.01)2
1 1 0 0 0 1 0 1
1 0 1 1
1
0
1
0
1

## Slide 5
Hexadecimal Number System
 Base = 16
 16 digits { 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B,
 Weights
C, D, E, F }
Position
256
16
1
1/16 1/256
 Weight = (Base)
 Magnitude
 Sum of “Digit x Weight”
 Formal Notation
2
1
0
-1
-2
1 *162+14 *161+5 *160+7 *16-1+10 *16-2
=(485.4765625)10
(1E5.7A)16
A
7
5
E
1

## Slide 6
The
Power
of
2
Kilo
Mega
Giga
Tera
n
2n
8
28=256
9
29=512
10
210=1024
11
211=2048
12
212=4096
20
220=1M
30
230=1G
40
240=1T
n
2n
0
20=1
1
21=2
2
22=4
3
23=8
4
24=16
5
25=32
6
26=64
7
27=128

## Slide 7
Addition
 Decimal
Addition
1
1
5
5
Carry
5
5
+
1
1
0
=
Ten ≥ Base
 Subtract a Base

## Slide 8
Binary Addition
 Column
Addition
1
1
1
1
1
1
1
1
0
1
1
1
1
0
1
1
1
=
=
61
23
+
=
84
1
0
1
0
1
0
0
≥ (2)10

## Slide 9
Binary Subtraction
 Borrow
a
“Base” when needed
1
2
0
2
0
1
1
= (10)2
0
1
2
0
1
0
1
0
2
0
1
1
1
=
=
77
23
−
0
1
1
0
1
1
0
=
54

## Slide 10
Binary
Multiplication
 Bit
by
bit
1
0
1
1
0
1
1
1
0
x
0
0
0
1
0
1
0
1
0
1
0
0
1
0
1
0
1
0
0
1
1
1
1
0
0
1
1
0

## Slide 11
Number Base Conversions
Evaluate
Magnitude
Octal
(Base
8)
Evaluate
Magnitude
Decimal
Binary
(Base 2)
(Base
10)
Hexadecimal
(Base 16)
Evaluate
Magnitude

## Slide 12
Decimal (Integer) to Binary Conversion
 Divide the number by the ‘Base’ (=2)
 Take the remainder (either 0
 Take the quotient and repeat
or 1) as a coefficient
the division
Example: (13)10
Coefficient
a0 = 1
a1 = 0
a2 = 1
a3 = 1
Quotient
6
3
1
0
Remainder
1
0
1
1
13 / 2 =
6 / 2 =
3 / 2 =
1 / 2 =
Answer:
(13)10 = (a3 a2 a1 a0)2 = (1101)2
MSB
LSB

## Slide 13
Decimal (Fraction) to Binary Conversion
 Multiply the number by the ‘Base’ (=2)
 Take the integer (either 0 or 1) as a coefficient
 Take the resultant fraction and repeat the
division
Example: (0.625)10
Coefficient
Integer Fraction
a-1
a-2
a-3
= 1
= 0
= 1
0.625 * 2 = 1
0.25 * 2 = 0
.
.
.
25
5
0
0.5
* 2 = 1
Answer:
(0.625)10 = (0.a-1 a-2 a-3)2 = (0.101)2
MSB
LSB

## Slide 14
Decimal to Octal Conversion
Example: (175)10
Coefficient
a0 = 7 a1 = 5 a2 = 2
Quotient
21
2
0
Remainder
7
5
2
175 / 8 =
21 / 8 =
2
/ 8 =
Answer:
(175)10 = (a2 a1 a0)8 = (257)8
Example: (0.3125)10
Coefficient
Integer Fraction
a-1
a-2
= 2
= 4
0.3125 * 8 = 2
.
.
5
0
0.5
* 8 = 4
Answer:
(0.3125)10 = (0.a-1 a-2 a-3)8 = (0.24)8

## Slide 15
Binary − Octal
Conversion
23
 8 =
 Each group
digit
of
3 bits represents an
octal
Assume Zeros
Example:
(
1 0 1 1 0
. 0 1
)2
(
2
6
. 2
)8
Works both
ways (Binary
to Octal &
Octal
to Binary)
Octal
Binary
0
0 0 0
1
0 0 1
2
0 1 0
3
0 1 1
4
1 0 0
5
1 0 1
6
1 1 0
7
1 1 1

## Slide 16
Binary − Hexadecimal
Conversion
24
 16 =
 Each group of 4 bits represents a
hexadecimal
digit
Assume Zeros
Example:
( 1 0 1 1 0
. 0 1
)2
( 1
6
. 4
)16
& Hex
Works both
ways (Binary
to Hex
to Binary)
Hex
Binary
0
0 0 0 0
1
0 0 0 1
2
0 0 1 0
3
0 0 1 1
4
0 1 0 0
5
0 1 0 1
6
0 1 1 0
7
0 1 1 1
8
1 0 0 0
9
1 0 0 1
A
1 0 1 0
B
1 0 1 1
C
1 1 0 0
D
1 1 0 1
E
1 1 1 0
F
1 1 1 1

## Slide 17
Octal − Hexadecimal Conversion
 Convert to Binary
Example:
(
as an
intermediate step
2
6
.
2
)8
Assume
Zeros
Assume
Zeros
( 0
1 0
1 1
0 .
0 1
0 )2
( 1
6
.
4
)16
Works both ways (Octal to Hex & Hex
to Octal)

## Slide 18
Decimal, Binary, Octal and Hexadecimal
Decimal
Binary
Octal
Hex
00
0000
00
0
01
0001
01
1
02
0010
02
2
03
0011
03
3
04
0100
04
4
05
0101
05
5
06
0110
06
6
07
0111
07
7
08
1000
10
8
09
1001
11
9
10
1010
12
A
11
1011
13
B
12
1100
14
C
13
1101
15
D
14
1110
16
E
15
1111
17
F

## Slide 19
Complements
 There are two types of complements for each base-r system: the radix complement and
diminished radix complement.
 Diminished Radix Complement - (r-1)’s Complement
 Given a number N in base r having n digits, the (r–1)’s complement
defined as:
(rn –1) – N
 Example for 6-digit decimal numbers:
 9’s complement is (rn – 1)–N = (106–1)–N = 999999–N
 9’s complement of 546700 is 999999–546700 = 453299
 Example for 7-digit binary numbers:
 1’s complement is (rn – 1) – N = (27–1)–N = 1111111–N
 1’s complement of 1011000 is 1111111–1011000 = 0100111
 Observation:
 Subtraction from (rn – 1) will never require a borrow
 Diminished radix complement can be computed digit-by-digit
 For binary: 1 – 0 = 1 and 1 – 1 = 0
of N
is

## Slide 20
Complements
 1’s Complement (Diminished Radix Complement)
 All ‘0’s become ‘1’s
 All ‘1’s become ‘0’s
Example (10110000)2
 (01001111)2
If you
add a
number and its 1’s complement …
1
0
0
1
1
0
1
0
0
1
0
1
0
1
0
1
+
1
1
1
1
1
1
1
1

## Slide 21
Complements
 Radix Complement
 Example: Base-10
 Example: Base-2
The 2's complement of 1101100 is 0010100
The 2's complement of 0110111 is 1001001
The 10's complement of 012398 is 987602
The 10's complement of 246700 is 753300
The r's complement of an n-digit number N in base r is defined as rn – N for N ≠ 0 and as 0 for N = 0. Comparing with the (r  1) 's complement, we note that the r's complement is obtained by adding 1 to the (r  1) 's complement, since rn – N = [(rn  1) – N] + 1.

## Slide 22
Complements
 2’s Complement (Radix Complement)
 Take 1’s complement then add 1
 Toggle all bits to the left of the first ‘1’ from the right
Example:
Number:
1’s Comp.:
OR
1
0
0
1
1
0
1
0
0
1
0
1
0
1
0
1
1
1 0 1
1 0 0 0 0
+
0
1
0
1
0
0
0
0
0 1 0
1 0 0 0 0