## Slide 1
Universality of
NAND & NOR Gates

## Slide 2: What are a Universal Gate ? Why NAND and NOR are known as universal gates?
A gate which can be used to create any Logic gate is called Universal Gate.
NAND and NOR are called Universal Gates because all the other gates can be created by using these gates.

## Slide 3: NAND as Universal Gates
Implementation of NOT using NAND
Desired [not gate]
F = A’
Available [Nand gate]
F = (A)’
F = A’

## Slide 4: NAND as Universal Gates
Implementation of NOT using NAND
A NOT gate is made by joining the inputs of a NAND gate together.
Desired NOT Gate
NOT using NAND

## Slide 5: NAND as Universal Gates
Implementation of AND using NAND
Desired [AND gate]
F=A.B
Available[NAND gate]
F=(A.B)’
To achieve AND gate;
F=[(A.B)’]’
F= A.B
A
B
(A.B)’
[(A.B)’]’ = A.B

## Slide 6: NAND as Universal Gates
Implementation of AND using NAND
An AND gate is made by following a NAND gate with a NOT gate(using NAND)
AND using NAND

## Slide 7: NAND as Universal Gates
Implementation of OR using NAND
Desired [OR gate]
F=A+B
Available[NAND gate]
F(A,B)=(A.B)’
= A’+B’
F(A’,B’)=(A’.B’)’
= A+B
A’
B’
(A’.B’)’
= A+B
A
B

## Slide 8: NAND as Universal Gates
Implementation of OR using NAND
An OR gate is made by inverting the inputs to a NAND gate.
OR using NAND

## Slide 9: NAND as Universal Gates
Implementation of NOR using NAND
A NOR gate is simply an inverted OR gate. So, we add NOT gate(using NAND) to OR gate made using NAND gates.
NOR using NAND

## Slide 10: NOR as Universal Gates
Implementation of NOT using NOR
Desired [not gate]
F = A’
Available [Nor gate]
F (A,A)= (A+A)’
F = A’

## Slide 11: NOR as Universal Gates
Implementation of NOT using NOR
NOT made by joining the inputs of a NOR gate.
NOR Gate
NOT using NOR

## Slide 12: NOR as Universal Gates
Implementation of OR using NOR
Desired [Or gate]
F = A+B
Available [NOR gate]
F = (A+B)’
F = [(A+B)’]’
F = (A+B)

## Slide 13: NOR as Universal Gates
Implementation of OR using NOR
The OR gate is simply a NOR gate followed by another
NOR gate
OR using NOR

## Slide 14: NOR as Universal Gates
Implementation of AND using NOR
Desired [AND gate]
F = A.B
Available [NOR gate]
F(A,B) = (A+B)’
F = A’.B’
F(A’,B’) = (A’+B’)’
F = A.B

## Slide 15: NOR as Universal Gates
Implementation of AND using NOR
AND using NOR
An AND gate is made by inverting the inputs to a NOR gate.
A’
B’
=(A’+B’)’
Q = A.B

## Slide 16: NOR as Universal Gates
Implementation of NAND using NOR
NAND using NOR
A NAND gate is simply an inverted AND gate. So, we add NOT gate(using NOR) to AND gate made using NOR gates.
F= A.B
= (A.B)’

## Slide 17: Summary

## Slide 18: NAND and NOR Implementation
NAND Implementation
1. Draw the logic diagram using basic gates. Assume both forms of wires are available.
2. Replace all the the AND gates using AND-invert symbol.
3. Replace all the OR gates using invert-OR symbol.
4. Cancel all the circles(inverters) in the same line. If any circle is remaining, replace it
using Inverter of NAND gate.
5. Replace all the remaining gates with AND-invert symbol.
Invert-OR
AND-invert
A
B
A
B
(A.B)’ = A’+B’
A’ +B’

## Slide 19: NAND and NOR Implementation
NAND Implementation
Implement the Boolean function F = A+(B’+C)(D’+BE’) using NAND gates only.
Step 1
Draw the logic diagram using basic gates. Assume both forms of wires are available.
A
B’
C
D’
B
E’
B’+C
BE’
D+BE’
(B’+C)(D+BE’)
F=A+(B’+C)(D+BE’)

## Slide 20: NAND and NOR Implementation
Step 2
Replace all the AND gates using AND-invert symbol.
A
B’
C
D’
B
E’

## Slide 21: NAND and NOR Implementation
Step 3
Replace all the OR gates using invert-OR symbol.
A
B’
C
D’
B
E’

## Slide 22: NAND and NOR Implementation
Step 4
Cancel all the circles in the same line.
A
B’
C
D’
B
E’
A
B’
C
D’
B
E’

## Slide 23: NAND and NOR Implementation
Step 5
Replace all the remaining gates with AND-invert gates.
.
A
B’
C
D’
B
E’

## Slide 24: NAND and NOR Implementation
Step 6
Simply, replace remaining circles with complementing the input or replace it with an inverter using NAND gate.
.
A’
B
C’
D
B
E’

## Slide 25: NAND and NOR Implementation
Finally, verify the output.
A’
B
C’
D
B
E’
T1
T2
T3
T4
F = A+(B’+C)(D’+BE’)

## Slide 26: NAND and NOR Implementation
Finally, verify the output.
T1 = (B.C’)’ = B’+C
T2 = (B.E’)’ = B’+E
T3 = (D.T2)’ = D’+T2’
T4 = (T1.T3)’ = T1’+T3’ = (B’+C)’ . (D’+T2’)’
= (B’+C)’ . (D’+(B’+E)’)’
F = (A’ .T4)’ = A + T4’
= A+[(B’+C)’+(D’+BE’)’]’
= A+(B’+C). (D’+BE’)

## Slide 27: NAND and NOR Implementation
F = (A+B’) (CD+E) using NAND gates only.

## Slide 28: NAND and NOR Implementation
NOR Implementation
1. Draw the logic diagram using basic gates. Assume both forms of wires are available.
2. Replace all the the OR gates using OR-invert symbol.
3. Replace all the AND gates using invert-AND symbol.
4. Cancel all the circles in the same line. If any circle is remaining, replace it using
Inverter of NOR gate.
5. Replace all the remaining gates with OR-invert signal.